SPECIFICATION

of work to be done and materials to be used in carrying

out the works shown on the accompanying drawings

~

(project name)

~

(project address)

~

(owners name)

Job Number:	~

Date:	~

# 4311M	METALCRAFT PROFILED ROOFING

## 1.	GENERAL

If you have pre-customised this work section using the "questions and answers" provided as part of the downloading process, it may be necessary to amend some clauses to suit the final project-specific version.

The section must still be checked and customised to suit the project being specified, by removing any other irrelevant details and adding project-specific details and selections.

This section relates to the supply and fixing of Metalcraft Roofing profiled roofing complete with accessories.

It includes:

-	Trough section roofing profiles

-	Asymmetrical rib roofing profiles

-	Corrugated roofing profile

-	Translucent roofing

Modify or extend the above description to suit the project being specified.

This section does not include for rainwater gutters, spouting and pipework.  Some flashing work is also covered elsewhere.

Note: In terms of NZBC E2/AS1, 8.4.4 Profiles, Metdek500 and Metdek855 roofing are classified as alternative solutions.

### 1.1	RELATED WORK

Refer to 4161 UNDERLAYS, FOIL AND DPC for underlays, foils and DPC.

Refer to ~ for ~.

Include cross references to other sections where these contain related work, such as.

Refer to 4311ME METALCRAFT ESPAN™ ROOFING for espan™ 340 trough roofing

Refer to 4312 PROFILED PLASTIC ROOFING for natural lighting sheeting.

Refer to 7411 RAINWATER SPOUTING SYSTEMS for rainwater disposal.

### 1.2	ABBREVIATIONS AND DEFINITIONS

The following abbreviations apply specifically to this section:

BMT	Base metal thickness

NZMRM	New Zealand Metal Roofing Manufacturers Inc

MS	Modified silicone

LBP	Licensed Building Practitioner

Refer general section 1232 INTERPRETATION & DEFINITIONS for abbreviations used throughout the specification.

Documents

### 1.3	DOCUMENTS

Refer to the general section 1233 REFERENCED DOCUMENTS.  The following documents are specifically referred to in this section:

NZBC E2/AS1	External moisture

NZBC G12/AS1	Water supplies

AS/NZS 1170.2	Structural design actions - Wind actions

AS 1397	Continuous hot-dip metallic coated steel sheet and strip - Coatings of zinc and zinc alloyed with aluminium and magnesium

AS 3566	Self-drilling screws for the building and construction industries

NZS 3604	Timber-framed buildings

ISO 9223	Corrosion of metals and alloys - Corrosivity of atmosphere - Classification determination and estimation

NZMRM CoP	NZ metal roof and wall cladding Code of Practice (CoP)

Delete from the DOCUMENTS clause any document not cited.  List any additional cited documents.

The following are related documents and if referred to in the work section need to be added to the list of DOCUMENTS.

BRANZ BU 318	Care of coil-coated metal claddings

BRANZ BU 358	Crest fixing of profiled metal roofing

BRANZ BU 408	Roofs on exposed sites

BRANZ BU 467	Principles of flashing design

BRANZ BU 519	Fasteners selection

BRANZ Good practice guide: Long-run metal roofing

NASH: Residential and Low Rise Steel Framing Part 1 2010 Design Criteria

### 1.4	MANUFACTURER/SUPPLIER DOCUMENTS

Manufacturer's and supplier's documents relating to this part of the work:

Metalcraft Roofing Metdek400 product literature

Metalcraft Roofing Metdek500 product literature

Metalcraft Roofing Metdek855 product literature

Metalcraft Roofing Metrib750 product literature

Metalcraft Roofing Metrib760 product literature

Metalcraft Roofing MC700 product literature

Metalcraft Roofing MC770 product literature

Metalcraft Roofing MC760 product literature

Metalcraft Roofing T-Rib product literature

Metalcraft Roofing MC1000 product literature

Metalcraft Roofing Metcom7 product literature

Metalcraft Roofing Metcom930 product literature

Metalcraft Roofing Corrugate 760 product literature

Metalcraft Roofing Alsynite Topglass® product literature

Manufacturer/supplier contact details

Company:	Metalcraft Roofing

Web:	www.metalcraftroofing.co.nz

Email:	frances.charles@unitedindustries.co.nz

Telephone:	09 274 0408

It is important to ensure that all personnel on site have access to accurate, up to date technical information on the many products, materials and equipment used on a project.  In most cases individual products are not used in isolation, but form part of a building process.  Also a particular manufacturer's and/or supplier's requirements for handling, storage, preparation, installation, finishing and protection of their product can vary from what might be considered the norm.  Access to technical information can help overcome this potential problem.

Warranties

Refer to SELECTIONS for a guide to typical warranty details for different systems.  They are a guide only, as project details may vary the warranty periods, check with Metalcraft Roofing to confirm warranties and recommended systems.

### 1.5	WARRANTY - MANUFACTURER/SUPPLIER

Provide a material manufacturer/supplier warranty:

~ years	for failure of coating adhesion

~ years	for weatherproofing  by material penetration

For Warranty requirements in excess of this contact Metalcraft Roofing.

Check general section 1237 WARRANTIES for the date of commencement of warranties; which is normally practical completion of the contract.  Refer to the chosen conditions of contract as it may also contain information on warranties and guarantees.

### 1.6	WARRANTY - INSTALLER/APPLICATOR

Provide an installer/applicator warranty:

5 years for workmanship

-	Provide this warranty on the material manufacturers standard warranty form.

-	Commence the warranty from the date of practical completion of the contract works.

Include a copy of the Metalcraft Roofing maintenance requirements with the warranty.

Refer to the general section 1237 WARRANTIES for additional requirements.

Check general section 1237 WARRANTIES for the date of commencement of warranties; which is normally practical completion of the contract.  Refer to the chosen conditions of contract as it may also contain information on warranties/guarantees.

Requirements

### 1.7	NO SUBSTITUTIONS

Substitutions are not permitted to any specified system, or associated components and products.

### 1.8	QUALIFICATIONS

Roof Installers shall be experienced, competent roofers familiar with Metalcraft products. And for Restricted Building Work shall also be, an LBP or supervised by an LBP.

Carry out work with experienced, competent installers familiar with the products being used and preferably with appropriate qualifications such as the National Certificate in Metal Roofing and Cladding.

Performance - wind

The next two mutually exclusive clauses, are setting a standard of performance for design by the contractor to meet. Specifiers should therefore consider adding some means of confirming (say by testing or certification) that the performance criteria will be or have been met. Delete the clause which does not apply.

### 1.9	WIND - NON SPECIFIC DESIGN

Building wind zone:

~ / ~kPa ULS (refer to NZS 3604, table 5.4)

Refer to Metacraft for "Wind Load Span Design Graphs" for load parameters.

Examples of design parameters include Wind Zone and NZS 3604.

Low /0.65kPa:	32 m/s

Medium /0.85kPa:	37 m/s

High /1.20kPa:	44 m/s

Very High /1.55kPa:	50 m/s

Extra High /1.62kPa:	55 m/s

Delete the clause if using WIND - SPECIFIC DESIGN

### 1.10	WIND - SPECIFIC DESIGN

The design wind pressures are to AS/NZS 1170.2:

SLS	~kPa

ULS	~kPa

Refer to Metalcraft for "Wind Load Span Design Graphs" for load parameters.

Obtain information from the project structural engineer.

Note;

-	For some situations Positive and Negative pressures will need to be stated.

-	Also for some situations Face and Edge Zone pressures will need to be stated.

-	Pressures may need to be expressed on a floor by floor basis.

-	For large or complex projects specifically marked up elevations may need to be referred to.

Delete the clause if using WIND - SPECIFIC DESIGN

### 1.11	FIXINGS, WIND

Design and use the fixings/fixing pattern appropriate for the wind design parameters and NZMRM CoP NZ metal roof and wall cladding Code of Practice.  Refer to Metalcraft profiled roofing product literature for profile details.  Allow for specific loadings at corners and the periphery of the roof, where localised pressure factors apply.  Fixing pattern to also take into account fixing method and purlin spacings.

Note; periphery areas, of any roof plane, generally have more fixings and reduced purlin spacings (non-NZS 3604 specific design), compared to the centre of the roof.

Performance - General

### 1.12	PERFORMANCE

Install roofing materials in accordance with the NZMRM CoP NZ metal roof and wall cladding Code of Practice, and Metalcraft profiled roofing product literature, to form a weather-tight performance for the completed roofing system, including all penetrations through the roof and junctions with walls and parapets.

Refer to later EXECUTION clause on co-operating with others on the installation of elements which penetrate or adjoin the roofing system; including walls and parapets, skylights, sundry elements fixed through the roofing surface, service pipework, etc.

### 1.13	DRINKING WATER

Roofing for collecting potable water to NZBC G12/AS1.

### 1.14	CO-ORDINATE

Co-ordinate to ensure substrate and preparatory work is complete and other work programmed in the order required for access and completion of the roof. Ensure that all necessary members are positioned so that flashings can be fastened at both edges through the roof profile or cladding to the primary structure.

## 2.	PRODUCTS

Materials

Select the product that suits the brief and use the PRODUCTS and EXECUTION clauses that follow to suit the product selected.

### 2.1	PRE-FINISHED HOT-DIPPED ALUMINIUM/ZINC COATED STEEL

Formability steel sheet, G550 for roll forming or G300 for flashings, coated to AS 1397.

Such as Pre-finished Zincalume®.

Where appropriate G300 steel sheet coated to AS 1397 can be used.

### 2.2	HOT-DIPPED ALUMINIUM/ZINC/MAGNESIUM COATED STEEL, UNPAINTED

Formability steel sheet, G550 for roll forming or G300 for flashings, coated to AS 1397.

Where appropriate G300 steel sheet coated to AS 1397 can be used.

Fixings

### 2.3	FASTENERS GENERALLY

Fixings and fasteners are to be compatible with all materials, the environment and meeting the requirements of the NZ Building Code. Installation is to be in accordance with E2/AS1 and/or the NZ Metal Roof and Wall Cladding - Code of Practice and Metalcraft profiled roofing product literature.

For fixing patterns refer to Metalcraft product literature for roofing profile.

### 2.4	FIXING SCREWS

To AS 3566. Screws appropriate to the roofing material and the supporting structure, as required by Metalcraft and with a Class 4 or 5 durability and not less than the material being fixed. Screws into timber to penetrate by minimum 30mm. Screw fasteners to be head stamped identifying the manufacturer and class. Refer to SELECTIONS.

For thermal movement refer to Metalcraft product literature for roofing profile.

Prepare a separate clause specifying profiled washers and oversized holes as required by the roofing manufacturer and consider detailing a step in the roofing (check details with the roofing manufacturer).

Length of fixing will depend on the height of the selected profile.  Check the roofing manufacturer's requirements.

Class 5 screws provide increased durability and must be used for Exposure Zone E to NZBC E2/AS1 (and C5 to ISO 9223)

Where thermal movement might exceed 6mm prepare a separate clause specifying profiled washers and oversized holes as required by the roofing manufacturer and consider detailing a step in the roofing or run onsite for long lengths in some profiles (check details with the roofing manufacturer).

### 2.5	RIVETS

Sealed aluminium, minimum diameter 4.0mm. Refer to Metalcraft for requirements..

Size depends on profile and project restraints. Check the roofing manufacturer's requirements..

### 2.6	FLASHINGS GENERALLY

Formable grade 0.55 BMT for galvanized, aluminium/zinc, aluminium/zinc/magnesium - coated and pre-painted steel and for Metdek500 (only) 0.70 BMT aluminium (or 0.7mm for small aluminium flashings) to the same standards as the profiled sheets, notched where across profile or provided with a soft edge.

Revise the clause wording to suit the specified roofing.

NZBC E2/AS1 does allow aluminium flashings of 0.7mm, this is only recommended for small flashings.

Components

### 2.7	FLASHINGS TO VERGE, RIDGE AND HIP

To NZBC E2/AS1, 4.0, Flashings.

Supplied by the roofing manufacturer to match or to suit the roofing.

For flashings and capping use low tensile grade G 300 steel.  If specifying aluminium/zinc-coated sheet use only compatible materials for soft edgings - soft pure aluminium 0.45mm thick, or Flashguard.

Accessories

### 2.8	WIRE NETTING AND SAFETY MESH

Refer to 4161 UNDERLAYS, FOIL AND DPC.

PVC coated netting is recommended for Zone D and Zone E exposure and other corrosive environments.  Wire netting is normally only used in areas where there is a low risk of falling.  It is required for pitches under 8º; and some wide purlin spacings, to support underlay. Safety mesh is used in high studs and open spans such as factories and storage facilities, and particularly under plastic roofing.  Generally used in all commercial applications.

### 2.9	UNDERLAY AND REFLECTIVE FOIL

Refer to 4161 UNDERLAYS, FOIL AND DPC.

### 2.10	SEALANT

Neutral curing silicone or polymer sealant as required by Metalcraft and used as directed.

### 2.11	CLOSURE STRIPS

Polyurethane profiled closed cell foam strips to fit the sheet profile.

Brand:	Ecofoam

Profile:	To suit selected cladding profile

## 3.	EXECUTION

Conditions

### 3.1	INSPECTION

Inspect the roof framing and supporting structure to ensure that it is complete and fully braced ready for roofing and free from any misalignments or protrusions that could damage the roofing.

### 3.2	FRAMING TIMBER MOISTURE

When continuous metal cladding etc. Runs along a long continuous timber member and is directly fixed to it, the timbers equilibrium moisture content (EMC) to be 18% or less.  For flashings in this situation (sometimes called transverse flashings) the framing EMC to be maximum 16%, and preferably as low as 12%.  Transverse flashings can be temporarily tacked in place and final fixing done when moisture content is acceptable.

Transverse flashings can be prone to buckling if there is excessive timber moisture movement.

### 3.3	STORAGE

Upon delivery visually inspect sheets for damage and accept packs of undamaged roofing.  Reject all damaged material.  Store on a level firm base clear of the ground, with packs well ventilated and completely protected from weather and damage.  Do not allow moisture to build up between sheets.  If sheet packs become wet, fillet or cross stack to allow air circulation and drying between sheets.

### 3.4	HANDLING

Do not drag sheets across each other or other materials.  Avoid distortion and contact with damaging substances, including cement.  Long lengths of roofing should be lifted onto the roof using an approved load spreading beam.  Protect edges and surface finishes from damage, keep under cover and remove as the product is being installed.  Use soft, flat sole shoes when fixing and for all other work on the roof.  Walk along the purlin line whenever possible.

### 3.5	SEPARATION

Isolate dissimilar materials (metals and non-metals) in close proximity as necessary by painting the surfaces or fitting separator strips of compatible materials.  Place isolators between metals and treated timber and cement based materials.  Do not use lead sheet or copper in contact with or allow water run-off onto galvanized or aluminium/zinc coated steel.

Application

The following execution clauses are written specifically to suit profiled, pre-coated galvanized steel, or aluminium/zinc coated steel.  If using aluminium or stainless steel they will need re-evaluating.

### 3.6	FIX INSULATION

Refer to thermal insulation sections.

### 3.7	SET-OUT

Carefully set out with consideration of the position of side laps to take account of the prevailing wind and line of sight.  Ensure all sheets are square and oversailing the gutter true to line.  Check during fixing to eliminate creep or spread and string lines along purlin centres to keep fastenings in line.

### 3.8	END LAPS

End laps are not recommended, except where specifically detailed.

### 3.9	THERMAL MOVEMENT

Fix for Thermal Movement to Metalcraft requirements for thermal movement.

### 3.10	FIXING GENERALLY

Install and fix in accordance with the NZMRM CoP recommendations, and to Metalcraft required fixing patterns and details for each area of the building roofing.  Use only screws as required by Metalcraft.  Paint colour matched fixings and accessories before installation.

### 3.11	MARKING AND CUTTING

Use ink pen, chalk line or coloured pencil for marking roof sheets prior to cutting.  Do not use lead pencil for marking Zincalume® and Colorsteel®.  Cut by shear only, using nibblers or hand snips.  Remove all cutting and drilling debris from the roof.

### 3.12	STOP ENDS AND DOWNTURNS

Form stop-ends at the upper end of sheets.  Form downturns at the gutter line where the roof pitch is less than 8 degrees.  Form using the required tools.

### 3.13	INSTALL FLASHINGS

Flash roof to parapets, walls and penetrations to detail.  Flashings to be installed on timber framing with moisture content of less than 20%.  Where no detail is provided flash to NZMRM CoP NZ metal roof and wall cladding Code of Practice recommendations and Metalcraft and NZBC E2/AS1 requirements.  Cut accurately and fix using sealant and rivets to detail and to Metalcraft requirements to form a weatherproof cover.  For visible flashings, plan joints/junction to take account of the aesthetic requirements.

### 3.14	USE OF SEALANTS

Select and use sealants only as recommended by Metalcraft.  Apply sealant in two narrow beads transversely across flashing intersections, close to the two edges.  Avoid exposing sealant on outside surfaces.

### 3.15	FLASHING PENETRATIONS

Flash all penetrations through the roof.  Fit pipe flashings with a proprietary collar flashing, with other penetrations flashed as detailed and to provide a weathertight installation.  Ensure that flashings are set to avoid any ponding of water.

Completion

### 3.16	REPLACE

Replace damaged or marked elements.  Do not attempt to repair coatings by applying colour match paint to pre-finished surfaces.

### 3.17	LEAVE

Leave this work complete with all necessary flashings, undercloaks, valleys, ridges and hips all properly installed as the work proceeds so the finished roof is completely weathertight.

### 3.18	REMOVE

Remove all trade rubbish, swarf and unused materials from the roof and surrounds daily during the work.  Sweep down at the end of each day, and clean out spouting, gutters and rainwater pipes on completion of the roof.  Remove debris, unused materials and elements from the site.

## 4.	SELECTIONS

For further details on selections go to www.metalcraftroofing.co.nz.

Substitutions are not permitted to the following, unless stated otherwise.

Selection of the correct grade of material and appropriate surface coating is imperative to ensure roofing profile will perform satisfactorily in the environment it is to be installed, and meets the requirements of the NZ Building Code.

SELECTIONS is for providing details of the actual selections to be included in the contract works including model numbers, colours and other information necessary to ensure that the correct materials are supplied and installed.

Colorsteel, Endura, Maxx, Zincalume and Galvsteel are registered trademarks of New Zealand Steel Limited.  Reference should be made to the coils and paint manufacturers own literature before choosing an appropriate finish.

Coating system

### 4.1	COATING SYSTEM - EXPOSURE ZONE B-C (CAT 1-3)

Project Exposure Zone B-C to NZS 3604, C 1-3 to ISO 9223.

Profile/location:	~

Base material:	~

Coating system:	~

Paint colour:	~

The following details are a guide only (typically domestic), as project details may vary the warranty periods, check with Metalcraft to confirm warranties and recommended system.

| COATING | BASE MATERIAL | COATING typical warranty | PERFORATION typical warranty |
| --- | --- | --- | --- |
| None | Zincalume® on steel (limitations apply) | NA | 15 years |
| Colorsteel Endura | Zincalume® on steel | 18 years | 30 years |
| Colorsteel Maxx | Zincalume® on steel | 15 years | 30 years |
| Colorcote AR8 | Aluminium | 18 years | 30 years |
| Colorcote ARX | Aluminium | 20 years | 30 years |

| COATING | BASE MATERIAL | COMPREHENSIVE typical warranty | LIGHT TRANSMISSION typical warranty |
| --- | --- | --- | --- |
| N/A | Alsynite Topglass® | 25 years | 15 years |
|  | Alysynite Topglass® GC | 25 years | 20 years |
|  | Alysynite Topglass® GC SPF | 25 years | 20 years |
|  | Alysynite Topglass® GC Ultra-Safe | 20 years | 10 years |
|  | Alysynite Twin-Skin | 25 years | 20 years |
|  | Alysynite Topglass® 50 FR | 25 years | 20 years |
|  | Alysynite Topclad® GC | 25 years | 20 years |

Unfinished galvanized steel is not recommended and should only be considered in non-critical buildings in Cat 1 exposure zones.

Note; Due to expansion, only light colours are recomended on long sheets.  This varies with materials and profiles, refer to Metalcraft for details.

### 4.2	COATING SYSTEM - EXPOSURE ZONE D (CAT 4)

Project Exposure Zone D to NZS 3604, C 4 to ISO 9223.

Profile/location:	~

Base material:	~

Coating system:	~

Paint colour:	~

The following details are a guide only (typically domestic), as project details may vary the warranty periods, check with Metalcraft to confirm warranties and recommended system.

| COATING | BASE MATERIAL | COATING typical warranty | PERFORATION typical warranty |
| --- | --- | --- | --- |
| Colorsteel Endura | Zincalume® on steel | 15 years | 15 years |
| Colorsteel Maxx | Zincalume® on steel | 15 years | 20 years |
| Colorcote AR8 | Aluminium | 15 years | 30 years |
| Colorcote ARX | Aluminium | 20 years | 30 years |

| COATING | BASE MATERIAL | COMPREHENSIVE typical warranty | LIGHT TRANSMISSION typical warranty |
| --- | --- | --- | --- |
| N/A | Alsynite Topglass® | 25 years | 15 years |
|  | Alysynite Topglass® GC | 25 years | 20 years |
|  | Alysynite Topglass® GC SPF | 25 years | 20 years |
|  | Alysynite Topglass® GC Ultra-Safe | 20 years | 10 years |
|  | Alysynite Twin-Skin | 25 years | 20 years |
|  | Alysynite Topglass® 50 FR | 25 years | 20 years |
|  | Alysynite Topclad® GC | 25 years | 20 years |

Note; Due to expansion, only light colours are recomended on long sheets.  This varies with materials and profiles, refer to Metalcraft for details.

### 4.3	COATING SYSTEM - EXPOSURE ZONE E (CAT 5)

Project Exposure Zone E to NZS 3604, C 5 to ISO 9223, plus geothermal.

Profile/location:	~

Base material:	~

Coating system:	~

Paint colour:	~

The following details are a guide only (typically domestic), as project details may vary the warranty periods, check with Metalcraft to confirm warranties and recommended system.

| COATING | BASE MATERIAL | COATING typical warranty | PERFORATION typical warranty |
| --- | --- | --- | --- |
| Colorsteel Maxx | Zincalume® on steel (limitations apply) | 15 years | 15 years |
| Colorcote ARX | Aluminium | 15 years | 20 years |

| COATING | BASE MATERIAL | COMPREHENSIVE typical warranty | LIGHT TRANSMISSION typical warranty |
| --- | --- | --- | --- |
| N/A | Alsynite Topglass® | 25 years | 15 years |
|  | Alysynite Topglass® GC | 25 years | 20 years |
|  | Alysynite Topglass® GC SPF | 25 years | 20 years |
|  | Alysynite Topglass® GC Ultra-Safe | 20 years | 10 years |
|  | Alysynite Twin-Skin | 25 years | 20 years |
|  | Alysynite Topglass® 50 FR | 25 years | 20 years |
|  | Alysynite Topclad® GC | 25 years | 20 years |

Note; Due to expansion, only light colours are recomended on long sheets.  This varies with materials and profiles, refer to Metalcraft for details.

Roofing - asymmetrical rib profile

### 4.4	METCOM7 ASYMMETRICAL RIB PROFILE ROOFING

Location:	~

Manufacturer:	Metalcraft Roofing

Profile:	METCOM7~

Dimensions:	Sheet width 933mm, cover 889mm, rib height 36mm, and roll formed to any length

Roof pitch:	~

BMT/material:	~

Purlin material:	~

Fixings:	~

Options:

Profile:	Straight or Drape curved (sprung curved).  (Refer to Metalcraft Roofing for guide for minimum radii for convex sprung curved and pre-curved roofing)

Dimensions:	Sheet width 933mm, cover 889mm, rib height 36mm, roll formed to any length, refer to Metalcraft for more information

Roof pitch:	Minimum 3°

BMT/materials:	0.40mm Steel, 0.55mm Steel, Translucent Alsynite (refer to TRANSLUCENT ROOFING clause)

Purlin Material:	Timber or Steel (steel thickness; up to 1.5mm, 1.5-4.5mm or 4.5-12mm)

FIXINGS FOR STEEL METCOM7 ROOFING

| PURLINS | FIXINGS | COMMENT |
| --- | --- | --- |
| Timber | Class 4 12G x 75mm or 14G x 90mm with load spreading washer |  |
| Steel up to 12mm | Class 4 12G x 65mm or 12G x 75mm with load spreading washer | Pre-drill steel if necessary |

Note: Change to Class 5 for Exposure Zone E to NZBC E2/AS1 (and C5 to ISO 9223)

Consult with Metalcraft for fixings for other roofing materials.

Translucent roofing

### 4.5	ALSYNITE TRANSLUCENT ROOFING

Location:	~

Brand:	Alsynite

Type:	~

Colour:	~

Options:

Type:	Alsynite Topglass®GC gel-coated natural roof lighting

Alsynite Topglass®GC SPF solar protective gel-coated

Alsynite Topglass® GC Ultra-Safe High impact corrosion resistant glass reinforced roofing and cladding

Alsynite Twin-Skin systems heat reducing translucent sheeting

Alsynite Topglass®  50 FR Plus Fire retardant translucent roofing

Colour:	Clear, Orchid, Opal, Cool, Bronze or Grey tint

Type:	Alsynite Topclad™ GC heavy duty, corrosion resistant, solid-coloured roofing and cladding system

Colour:	Available in solid colours to match roofing colour

Manufactured to suit roofing profile for commercial applications.

Accessories

### 4.6	FLASHINGS - GENERALLY

Profile:	~

BMT/material:	~

Coating system:	To match roofing

Paint colour:	To match roofing

BMT options:	0.55mm Steel, 0.7mm Aluminium

Modify colour and coating if necessary.